## Slide 1
INTRODUCTION TO
RISC-V Architecture
A complete beginner's guide to the open-source Instruction Set Architecture
From basic concepts to pipeline stages and extensions
Notes: 1

## Slide 2
What We'll Cover
01
02
What is RISC-V ISA and why PicoRV32 for our SoC Subsystem?
32 registers (x0–x31) — their role in firmware execution
03
Instruction formats — how rom.hex words map to RISC-V opcodes
04
PicoRV32 native memory interface (mem_valid / mem_ready)
05
Lab: make pico — run PicoRV32 standalone simulation
06
Waveform: observe instruction fetch cascade in GTKWave
Notes: 2

## Slide 3
What is an Instruction Set Architecture (ISA)?
Think of an ISA like a restaurant menu. The menu (ISA) lists all dishes (instructions) the kitchen (hardware) can make. Software is the customer who orders from the menu — it doesn't need to know HOW the kitchen works, only WHAT it can order.
Analogy:
What it defines
• The list of valid CPU instructions
• How memory is addressed
• How registers are used
• How the OS talks to hardware
Why it matters
• Software written for one ISA runs on ALL chips that implement it
• Separates hardware design from software design
• Enables a huge ecosystem of tools & compilers
Examples
• x86 — Used in most PCs
• ARM — Used in phones & tablets
• MIPS — Used in routers
• RISC-V — Open source, growing fast
Notes: 4

## Slide 4
RISC vs CISC — Two Design Philosophies
Feature
RISC (Reduced Instruction Set)
CISC (Complex Instruction Set)
Instruction count
Few, simple instructions
Many, complex instructions
Instruction length
Fixed (e.g. 32-bit)
Variable length
Clock cycles/instr
Usually 1 cycle each
1 to many cycles
Memory access
Load/store model only
Any instruction can access memory
Hardware
Simple, smaller chip area
Complex decoder circuitry
Examples
ARM, MIPS, RISC-V
x86, x86-64 (Intel/AMD)
Best for
Embedded, mobile, efficiency
Legacy desktop apps, x86 ecosystem
Notes: 6

## Slide 5
RISC-V Overview
Born
UC Berkeley, 2010 — free, open, royalty-free ISA
Base ISA
RV32I / RV64I — fixed 32-bit instructions
Modular
Optional extensions: M (mul), F (float), V (vector)…
Governed
RISC-V International — non-profit standards body
This Project
PicoRV32 — minimal RV32I in ~3100 lines of Verilog
Open-Source ISA — Origin & Ecosystem
Notes: 8

## Slide 6
PicoRV32 — The CPU in This Project
File: rtl/picorv32.v (~3100 lines of pure Verilog RTL) · ISA: RV32I — complete base integer instruction set only
.ENABLE_COUNTERS
(1)
cycle/instret counters ON
.ENABLE_REGS_16_31
(1)
full 32-register file
.ENABLE_MUL
(0)
NO multiply (saves area)
.ENABLE_DIV
(0)
NO divide
.COMPRESSED_ISA
(0)
NO 16-bit instructions
.CATCH_ILLINSN
(1)
trap on illegal instruction
.CATCH_MISALIGN
(1)
trap on misaligned access
.PROGADDR_RESET
(0x0000_0000)
boot addr = ROM[0]
.STACKADDR
(0x0001_00FC)
stack top
OUTPUT
mem_valid
Request pending
OUTPUT
mem_instr
1=fetch 0=data
OUTPUT
mem_addr[31:0]
Target address
OUTPUT
mem_wdata[31:0]
Write data
OUTPUT
mem_wstrb[3:0]
Byte enable
INPUT
mem_ready
Transaction OK
INPUT
mem_rdata[31:0]
Read data
INPUT
resetn
Active-low reset
⚙ Configuration Parameters
🔌 Key I/O Ports

## Slide 7
RISC-V Registers (x0-x31)
Analogy: Registers are like your desk. RAM is the filing cabinet. Disk is the warehouse. You work with what's on your desk — fast access, but limited space (only 32 slots!).
x0 (zero)
Always reads as 0. Writes are ignored.
x1 (ra)
Return address — where to go back after a function call.
x2 (sp)
Stack pointer — tracks the top of the call stack.
x3 (gp)
Global pointer — base address of global variables.
x4 (tp)
Thread pointer — used in multi-threaded programs.
x5–x7 (t0–t2)
Temporaries — scratch registers, not preserved across calls.
x8 (s0/fp)
Saved register / frame pointer.
x9 (s1)
Saved register, preserved across function calls.
x10–x11 (a0–a1)
Function arguments 1 & 2, also return values.
x12–x17 (a2–a7)
Additional function arguments (up to 8 total).
x18–x27 (s2–s11)
Saved registers — callee must restore if used.
x28–x31 (t3–t6)
More temporaries — fast scratch space.
Notes: 10

## Slide 8
RISC-V Instruction Formats
All instructions are exactly 32 bits wide. The bits are arranged in 6 different patterns (formats) depending on the instruction type.
R-type
Register-to-register ops (ADD, SUB, AND…)
funct7 | rs2 | rs1 | funct3 | rd | opcode
I-type
Immediate arithmetic & loads (ADDI, LW…)
imm[11:0] | rs1 | funct3 | rd | opcode
S-type
Store to memory (SW, SB, SH…)
imm[11:5] | rs2 | rs1 | funct3 | imm[4:0] | opcode
B-type
Conditional branches (BEQ, BNE, BLT…)
imm[12|10:5] | rs2 | rs1 | funct3 | imm[4:1|11] | opcode
U-type
Upper immediate (LUI, AUIPC)
imm[31:12] | rd | opcode
J-type
Jump and link (JAL)
imm[20|10:1|11|19:12] | rd | opcode
Notes: 12

## Slide 9
Instruction Types & PicoRV32 Config Flags
✔
Integer Arithmetic
ADD, SUB, ADDI, LUI, AUIPC
✔
Logic
AND, OR, XOR, ANDI, ORI, XORI
✔
Shift
SLL, SRL, SRA, SLLI, SRLI, SRAI
✔
Compare
SLT, SLTU, SLTI, SLTIU
✔
Loads / Stores
LW, LH, LB, SW, SH, SB
✔
Branches
BEQ, BNE, BLT, BGE, BLTU, BGEU
✔
Jumps
JAL, JALR
✘
Multiply (M ext.)
MUL, MULH, DIV, REM
✘
Compressed (C ext.)
16-bit encodings
Config Flags
ENABLE_MUL=0, ENABLE_DIV=0
COMPRESSED_ISA=0
BARREL_SHIFTER=0
First Instruction
0x00020137 = LUI x2, 0x20
→ Sets up stack pointer at boot
Compiler Flag
-march=rv32i -mabi=ilp32
Matches ENABLE_MUL=0 exactly
mem_instr Signal
=1 → instruction fetch
=0 → data access (LW/SW)
📋 Instruction Support
🔧 Project-Specific Notes
Notes: 14

## Slide 10
CPU Pipeline: IF / ID / EX / MEM / WB
Pipelining lets the CPU work on multiple instructions at the same time — like an assembly line.
IF
Instruction
Fetch
Read next instruction from memory using the PC register.
ID
Instruction
Decode
Decode the opcode, read source registers, generate control signals.
EX
Execute
ALU performs computation: add, subtract, compare, shift, etc.
MEM
Memory
Access
Load from or store to data memory (only LW/SW instructions).
WB
Write
Back
Write the result back to the destination register.
⚠ PicoRV32 Stall Rule: CPU holds mem_valid=1 and freezes ALL signals until peripheral asserts mem_ready=1 (one cycle pulse). Only ONE outstanding transaction at a time — no out-of-order execution.
mem_valid=1
mem_instr=1
PC → mem_addr
Decode opcode
Read rs1, rs2
Sign-extend imm
ALU operation
Branch compare
Address calc
mem_valid=1
Stall until
mem_ready=1
mem_rdata →
register file
Update rd
Notes: 16

## Slide 11
Signal | Direction | Width | Description
mem_valid | CPU→MEM | 1 | Request pending — hold HIGH until mem_ready
mem_instr | CPU→MEM | 1 | 1 = instruction fetch, 0 = data access
mem_addr | CPU→MEM | 32 | Target address
mem_wdata | CPU→MEM | 32 | Write data (stores only)
mem_wstrb | CPU→MEM | 4 | Byte write enable: 0=read, 0xF=32-bit write
mem_ready | MEM→CPU | 1 | Transaction accepted (one-cycle pulse)
mem_rdata | MEM→CPU | 32 | Read data — valid same cycle as mem_ready
1
1
CPU drives mem_valid=1 and holds ALL signals stable
2
2
Memory / Peripheral asserts mem_ready=1 when ready
3
3
Transfer occurs at the clock edge when BOTH are HIGH
4
4
Only ONE outstanding transaction (CPU stalls pipeline)
PicoRV32 Native Memory Interface
⟳ Handshake Rule

## Slide 12
Branch Hazards & PicoRV32 Trap Behavior
TWO_STAGE_SHIFT · CATCH_ILLINSN · trap Signal
🔀 Branch Hazards (General)
Branch outcome not known until EX stage
Naïve pipeline fetches next sequential instruction
If branch taken → fetched instruction must be flushed
Flush = wasted cycle (1 pipeline bubble for PicoRV32)
PicoRV32 resolves branches in EX — simple stall, no speculation
⚙ PicoRV32-Specific Behavior
TWO_STAGE_SHIFT=1
Area optimization: shift ops take 2 cycles instead of 1. Saves LUTs in FPGA/ASIC implementation.
CATCH_ILLINSN=1
Any undefined opcode raises the trap signal. Firmware can detect and handle CPU halt.
CATCH_MISALIGN=1
Unaligned LW/SW (addr not multiple of 4) raises trap — important for AXI peripheral access.
trap Signal
Goes HIGH when CPU hits illegal instruction or misaligned access. Not exposed at top-level in current design but observable in testbench.
Notes: 18

## Slide 13
Lab: make pico — Run PicoRV32 Simulation
Navigate to project root
$ cd /path/to/picorv32_soc
Ensure Makefile is present in this directory
Run standalone PicoRV32 simulation
$ make pico
Builds firmware → Verilator compiles RTL → runs ./obj_pico/sim_pico → produces tb_picorv32.vcd
Open waveform in GTKWave
$ gtkwave tb_picorv32.vcd & OR: make wave
Add signals manually or load saved .gtkw config
Signals to ADD in GTKWave: clk · resetn · mem_valid · mem_instr · mem_ready · mem_addr[31:0] · mem_rdata[31:0]
1
2
3

## Slide 14
RISC-V Ecosystem → THIS Project
THIS PROJECT
PicoRV32 + AXI-Lite + UART SoC on SkyWater 130nm
$ make pico
→
Run PicoRV32 standalone simulation → tb_picorv32.vcd
$ make synth
→
Synthesize SoC with Yosys → gate-level netlist
Full physical design: floorplan → routing → GDS-II
$ make wave
→
Open waveform: gtkwave tb_picorv32.vcd
Broader RISC-V domains: IoT, AI Edge, Linux servers, automotive, space — our SoC is the hands-on proof-of-concept for this course.
Simulated: Verilator
Synthesized: Yosys
PnR: OpenLane
SkyWater 130nm PDK

## Slide 15
Sub-module 1 - Key Takeaways
PicoRV32 is RV32I
32 registers, fixed 32-bit instruction width, in-order execution. No mul/div/float in this project.
Native Bus Protocol
mem_valid + mem_ready — simple stall protocol. CPU holds all signals until peripheral responds.
Boot & Stack
PC starts at 0x0000_0000 → First instruction: LUI x2, 0x20 (stack init). Stack top: 0x0001_00FC.
Config Matters
ENABLE_MUL=0, ENABLE_DIV=0, COMPRESSED_ISA=0. Compiler must match: -march=rv32i -mabi=ilp32.
Run the Lab
make pico → Verilator simulation → tb_picorv32.vcd → GTKWave.
Watch the Waveform
mem_addr increments 0x0→0x4→0x8. mem_instr=1 on every fetch. First rdata=0x00020137.