## Slide 1
Sub-module 2
AXI4-Lite Protocol
Introduction & Architecture for PicoRV32 SoC Subsystem
From master-slave channels to handshake protocol
Notes: 1

## Slide 2
What We’ll Cover
What is AXI4-Lite?
02
AXI4-Lite vs AXI4-Full
03
5 Channels Overview Table
04
Channel Signal Diagram
05
Write Transaction Flow (AW→W→B)
06
Read Transaction Flow (AR→R)
07
VALID/READY Rules
08
Lab: make axi_sa
09
Summary
01
Notes: 2

## Slide 3
What is AXI4-Lite?
AXI4-Lite (Advanced eXtensible Interface 4-Lite) is a simplified subset of ARM's AMBA AXI4 bus protocol. Designed for low-throughput, register-mapped control interfaces where simplicity and low-area are priorities over raw bandwidth.
Developed By
ARM Ltd. (now Arm Holdings)
Part of the AMBA 4 specification
Single data-beat transfers only
No burst support
32-bit or 64-bit address
32-bit data width (standard)
Use Case
Control registers & status reads
Low-speed peripheral configuration
Transaction Type
Address Space
Notes: 4

## Slide 4
AXI4-Lite vs AXI4-Full
Feature | AXI4-Lite | AXI4-Full
Burst Transfers | ✗ Not supported | ✓ Up to 256 beats
Transaction IDs | ✗ None | ✓ Multi-ID OoO
Cache / Protect Signals | ✗ Not included | ✓ Full signaling
Register Access | ✓ Ideal (single TX) | ✓ Supported
Implementation Area | ✓ Very small | ✗ Large (queues, IDs)
Interconnect Lines | ✓ ~35 signals | ✗ 100+ signals
Why AXI4-Lite for THIS SoC? Single outstanding TX · Register-level peripheral access · No burst needed for UART/ROM · Minimal area (227-line interconnect)

## Slide 5
The 5 AXI4‑Lite Channels Overview
AW
M → S
Write Address
Signals
awaddr[31:0]
awvalid · awready
Master sends the destination write address to the slave
W
M → S
Write Data
Signals
wdata[31:0]
wstrb[3:0] · wvalid · wready
Master sends write data + byte-enable strobes to slave
B
S → M
Write Response
Signals
bresp[1:0]
bvalid · bready
Slave acknowledges the write — OKAY (2'b00) in this project
AR
M → S
Read Address
Signals
araddr[31:0]
arvalid · arready
Master sends the source read address to the slave
R
S → M
Read Data
Signals
rdata[31:0]
rresp[1:0] · rvalid · rready
Slave returns the read data + status to the master
Golden Rule: A transfer occurs ONLY when VALID = 1 AND READY = 1 at the rising clock edge — on ALL five channels
Notes: 5

## Slide 6
Channel Signal Diagram — THIS Project
MASTER
CPU-to-AXI Bridge
(top.v lines 91–224)
m_axi_awaddr
m_axi_awvalid / awready
m_axi_wdata
m_axi_wstrb
m_axi_wvalid / wready
m_axi_bvalid / bready
m_axi_araddr
m_axi_arvalid / arready
m_axi_rdata
m_axi_rvalid / rready
SLAVES (×3)
S0: ROM
rom.v
0x0000_0000
S1: SRAM
sram.v
0x0001_0000
S2: UART
uart_axi.v
0x1000_0000
AW
Write Address
W
Write Data
B
Write Response
AR
Read Address
R
Read Data
axi_lite_interconnect.v axi_decoder.v (one-hot sel)
wr_sel / rd_sel 001=ROM · 010=SRAM · 100=UART

## Slide 7
AXI4-Lite in THIS SoC — 1 Master, 3 Slaves
CPU-to-AXI Bridge
(top.v, lines 91–224)
AXI-Lite Interconnect (axi_lite_interconnect.v — 227 lines)
+ Address Decoder (axi_decoder.v — 165 lines)
S0: ROM
(rom.v)
S1: SRAM
(sram.v)
S2: UART
(uart_axi.v)
Address Range | Slave | casez Pattern
0x0000_???? | S0: ROM | 32'h0000_????
0x0001_???? | S1: SRAM | 32'h0001_????
0x1000_000? | S2: UART | 32'h1000_000?
default | → ROM (safe fallback) | —
Routing Signals
wr_sel[2:0] — one-hot write select
rd_sel[2:0] — one-hot read select
wr_active / rd_active

## Slide 8
Write Transaction : AW → W → B
A write transaction uses 3 channels in sequence: Write Address (AW) → Write Data (W) → Write Response (B)
AW
Step 1 — Write Address
Master drives awaddr + awvalid = 1
Slave asserts awready = 1
AW Handshake COMPLETE ✅
W
Step 2 — Write Data
Master drives wdata, wstrb, wvalid = 1
Slave asserts wready = 1
W Handshake COMPLETE ✅
B
Step 3 — Write Response
Slave asserts bvalid = 1, bresp = 2'b00
Master asserts bready = 1
B Handshake COMPLETE ✅
⚡ AW and W channels are independent — they can handshake simultaneously or in any order!
Notes: 6

## Slide 9
AXI Write — CPU Sends 'H' to UART TX Register
Firmware: uart_putc('H') → UART_TX = 0x1000_0000 → wdata = 0x0000_0048
Step 1: AW — Write Address Channel
CPU bridge → awaddr = 0x1000_0000, awvalid = 1
Interconnect → wr_sel = 3'b100 (UART selected)
uart_axi → awready = 1 (if not busy)
✅ AW Handshake complete
Step 2: W — Write Data Channel
CPU bridge → wdata = 0x0000_0048, wstrb = 4'h1, wvalid = 1
uart_axi → wready = 1 (if buffer not full)
uart_axi captures: w_byte = 0x48, buf_valid = 1
✅ W Handshake complete
Step 3: B — Write Response Channel
uart_axi → bvalid = 1, bresp = 2'b00 (OKAY)
CPU bridge → bready = 1
Bridge asserts cpu_mem_ready = 1 → CPU resumes
✅ B Handshake complete — UART TX buffer = 0x48 ('H')
Result: UART TX buffer filled with 0x48 ('H') → uart_tx FSM serializes as 8N1 on uart_tx pin

## Slide 10
Read Transaction Flow: AR → R
A read transaction uses 2 channels: Read Address (AR) → Read Data (R). Simpler than write — no response channel needed.
AR
Step 1 — Read Address
Master drives araddr + arvalid = 1
Slave asserts arready = 1
AR Handshake COMPLETE ✅
R
Step 2 — Read Data
Slave drives rdata + rvalid = 1
Master asserts rready = 1
R Handshake COMPLETE ✅
→
Timing (no wait-states):
Cycle 1: araddr=0x4, arvalid=1 → arready=1 (AR handshake)
Cycle 2: rvalid=1, rdata=0xA5A5A5A5 → rready=1 (R handshake)
Notes: 7

## Slide 11
AXI Read — CPU Polls UART Status Register
Firmware: uart_getc() → poll UART_STATUS (0x1000_0008) & 0x2
Step 1: AR — Read Address Channel
CPU bridge → araddr = 0x1000_0008, arvalid = 1
Interconnect → rd_sel = 3'b100 (UART selected)
uart_axi → arready = 1
✅ AR Handshake complete
Step 2: R — Read Data Channel
uart_axi prepares: rdata = {30'b0, rx_buf_valid, 1'b0}
uart_axi → rvalid = 1, rdata = 0x0000_0002 (RX ready)
CPU bridge → rready = 1
✅ R Handshake complete
Firmware checks: (UART_STATUS & 0x2) != 0 → data available in RX buffer

## Slide 12
VALID/READY Handshake Rules
GOLDEN RULE: Transfer occurs ONLY when VALID = 1 AND READY = 1 at the rising clock edge
1
VALID may be asserted without READY. The sender waits.
2
READY may be asserted without VALID. The receiver is ready to accept.
3
Once VALID is asserted, it MUST NOT be de-asserted until the handshake completes.
4
READY can be de-asserted freely between transactions.
5
Master must NOT make VALID dependent on READY (no circular deadlock).
6
Transfer data is captured by the receiver on the handshake clock edge.
Notes: 8

## Slide 13
WSTRB — Write Strobe Byte Enable
What is WSTRB?
4-bit signal (one bit per byte lane) indicating which bytes of wdata[31:0] are valid. Allows sub-word writes without a read-modify-write cycle.
WSTRB bit | Byte lane | wdata bits
wstrb[0] | Byte 0 | [7:0]
wstrb[1] | Byte 1 | [15:8]
wstrb[2] | Byte 2 | [23:16]
wstrb[3] | Byte 3 | [31:24]
Project Examples — Firmware → WSTRB Mapping
SW x0, 0(UART_BASE)
WSTRB = 4'hF
Full 32-bit word write — all 4 bytes valid
SB x0, 0(UART_BASE)
WSTRB = 4'h1
Byte write — only wdata[7:0] (byte 0) is valid
uart_axi.v — byte selection from WSTRB:
if (s_axi_wstrb[0]) w_byte <= s_axi_wdata[ 7: 0];
else if (s_axi_wstrb[1]) w_byte <= s_axi_wdata[15: 8];

## Slide 14
Write & Read Transaction Flow Summary
✍️ WRITE Transaction
1
AW
awaddr + awvalid → awready
2
W
wdata, wstrb, wvalid → wready
3
B
bvalid, bresp ← bready
📖 READ Transaction
1
AR
araddr + arvalid → arready
2
R
rvalid, rdata, rresp ← rready
2'b00 = OKAY (all transactions in this project) 2'b10 = SLVERR (slave error) 2'b11 = DECERR (decode error — check address map)
RESP Encoding:
Notes: 10

## Slide 15
BREADY
IN
1-bit
Master: ready to accept response
Why AXI4-Lite for THIS SoC?
⚡
Simplicity
No burst logic — perfect for UART/ROM serving one word at a time. Simple FSM in top.v.
🔓
Decoupling
AW and W channels let the CPU pipeline address and data separately, improving throughput.
♻️
Reuse
All 3 slaves (ROM, SRAM, UART) share one 35-signal AXI interface via the interconnect.
🪶
Area
rtl/axi_lite_interconnect.v = 227 lines — extremely lightweight for a 1M→3S fabric.
🔬
Verification
Independent channels enable isolated testing: make axi_sa tests handshake alone without RTL.
🏭
Industry Std.
ARM AMBA AXI4-Lite is the go-to choice for register-mapped peripherals in RISC-V SoC designs.
Notes: 11

## Slide 16
Lab: make axi_sa — Standalone AXI-Lite Handshake Demo
$ make axi_sa → ./obj_axi_sa/sim_axi_sa → tb_axi_lite_standalone.vcd (3.8 KB)
Expected Terminal Output:
[WRITE] Address = 0x00000004
[WRITE] Data = 0xa5a5a5a5
[WRITE] awready=1 → Handshake Done
[WRITE] bvalid=1 → Write Response Received (OKAY)
[READ] Address = 0x00000004
[READ] rvalid=1 → Data Received = 0xa5a5a5a5
[CHECK] Write Data == Read Data → PASS ✓
GTKWave Signals:
clk, reset
awaddr[31:0], awvalid, awready
wdata[31:0], wstrb[3:0], wvalid, wready
bvalid, bready, bresp[1:0]
araddr[31:0], arvalid, arready
rdata[31:0], rvalid, rready
All Sub-module 2 Lab Commands:
Command | Output VCD/FST | Tests
make axi_sa | tb_axi_lite_standalone.vcd | AXI handshake only
make axi_uart | tb_axi_lite.vcd | AXI + UART slave
make riscv_axi | tb_riscv_axi_lite.vcd | CPU bridge + AXI
make soc | tb_top.fst | Complete SoC

## Slide 17
Key Takeaways
5 Channels: AW (write addr) + W (write data) + B (write resp) + AR (read addr) + R (read data)
Address Map: ROM = 0x0000_0000 | SRAM = 0x0001_0000 | UART = 0x1000_0000
Golden Rule: Transfer occurs ONLY when VALID AND READY = 1 at rising clock edge
Lab: make axi_sa → write 0xA5A5A5A5 → read back → PASS ✓
THIS Project: 1 CPU bridge master ↔ 3 slaves via axi_decoder.v one-hot select
WSTRB: firmware SB → WSTRB=4'h1 → uart_axi selects wdata[7:0] as TX byte
Notes: 13