## Slide 1
Sub-module 3
UART
Serial Protocol
A Brief Description of UART
From start bits to baud rate — everything you need to know

## Slide 2
What We'll Cover
01
02
What is UART?
How UART Works?
03
UART Frame Structure
04
UART TX FSM (rtl/uart_tx.v)
05
UART RX FSM (rtl/uart_rx.v)
06
Baud Rate & Project Configuration
07
Lab Command
08
Waveform Debug
09
Real-World Applications

## Slide 3
What is UART?
UART (Universal Asynchronous Receiver-Transmitter) is one of the oldest and most widely used serial communication protocols. It transmits data bit-by-bit over a single wire per direction, without a shared clock signal — making it simple, low-cost, and universally supported.
Developed By
Originally from the 1960s
Popularised with RS-232 standard
Standardised across all MCUs
Signal Type
Asynchronous — no clock line
TX & RX lines only
Full-duplex capable
Data Format
Start bit + 5-9 data bits
Optional parity bit
1 or 2 stop bits
Use Case
Debug consoles & logging
GPS, GSM, BT modules
MCU-to-MCU links

## Slide 4
How UART Works
UART uses two wires — TX (transmit) and RX (receive). Each side sends and receives independently, with no shared clock. Both devices must agree on the same baud rate.
1 Idle State
The TX line sits HIGH (logic 1) when no data is being sent. Both devices wait at idle — this is the resting voltage.
2 Start Bit
Sender pulls TX LOW (logic 0) for exactly one bit period. This signals the receiver: 'data is coming — start your clock!'
3 Data Bits
5–9 data bits are sent LSB-first. Each bit lasts exactly 1/baud-rate seconds. Receiver samples mid-bit for accuracy.
4 Parity Bit (optional)
An optional error-detection bit. Even parity: total 1s are even. Odd parity: total 1s are odd. Can be omitted (None).
5 Stop Bit(s)
TX returns HIGH for 1 or 2 bit periods. Signals end of frame and gives receiver time to prepare for the next byte.

## Slide 5
UART Frame Structure
A single UART frame (byte transmission) consists of: Start → Data → Parity → Stop
IDLE
HIGH
START
LOW (0)
D0
LSB
D1
D2
D3
D4
D5
D6
D7
MSB
PAR
OPT
STOP
HIGH (1)
Start Bit
Always logic LOW. Triggers receiver to begin sampling. Duration = 1 / baud rate.
Data Bits (5–9)
Payload bits sent LSB first. Standard UART uses 8 bits (one full byte). Receiver samples mid-bit.
Parity Bit
Optional single-bit error check. Even, Odd, or None (most common). Cannot correct errors, only detect.
Stop Bit(s)
1 or 2 bits at logic HIGH. Marks end of frame. Gives receiver time to reset before next start bit.
Example: 'H' = 0x48 = 0100_1000 → TX: 0 0 0 0 1 0 0 1 0 1 (Start | D0→D7 LSB-first | Stop)

## Slide 6
UART TX FSM — rtl/uart_tx.v
IDLE 2'b00
tx = 1 (HIGH) Wait for valid=1 Load shift_reg
START 2'b01
tx = 0 (start bit) Count 434 cycles then → DATA
DATA 2'b10
tx = shift_reg[0] Shift right each bit bit_cnt 0→7 (×8)
STOP 2'b11
tx = 1 (stop bit) Count 434 cycles then → IDLE
→
→
→
← STOP → IDLE (after 434 cycles)
Ports:
clk, reset — system clock & active-high reset
data[7:0] — byte to transmit
valid — pulse: assert HIGH for 1 cycle when data is ready
ready — HIGH when TX is in IDLE (accepting new byte)
tx — serial output line (connect to RX pin of receiver)
Key Registers:
shift_reg[7:0] — loaded from data; right-shifted each bit-period; bit[0] → tx
clk_cnt[9:0] — baud counter: counts 0 → 433 (= CLKS_PER_BIT − 1)
bit_cnt[2:0] — data bit counter: counts 0 → 7 in DATA state

## Slide 7
UART RX FSM — rtl/uart_rx.v
2-FF Synchronizer — Why It Exists
External rx arrives asynchronously — its edges may not align to our 50 MHz clock. Capturing such a signal directly risks metastability: the flip-flop may output an undefined voltage for an unknown duration. Fix: 2-stage flip-flop chain: rx → rx_sync0 → rx_sync1 → rx_s (safe, clock-domain-crossed)
IDLE
Monitor rx_s for falling edge (start bit). Detect 0 → goto START
START
Wait 217 cycles (half-bit) then sample. Still 0? → DATA. 1? → IDLE
DATA
Sample rx_s at mid-bit every 434 cycles (×8). shift_reg ← {rx_s, [7:1]}
STOP
Wait 434 cycles. rx_s=1: data_out←shift_reg data_valid pulses 1 cycle
→
↓
←
↑
Output: data_out[7:0] — received byte (valid on data_valid pulse)
data_valid — single-cycle HIGH pulse per successfully received byte
Mid-bit timing: CLKS_HALF_BIT = CLKS_PER_BIT / 2 = 434 / 2 = 217
→ RX waits 217 cycles after detecting start bit before first sample
→ Subsequent bits sampled every 434 cycles (mid-bit of each DATA bit)

## Slide 8
Baud Rate & Project Configuration
50 MHz Clock · 115200 Baud · CLKS_PER_BIT = 434
Project Calculation
CLK_FREQ = 50,000,000 Hz (50 MHz) BAUD_RATE = 115,200 baud ───────────────────────────────────── CLKS_PER_BIT = 50,000,000 ÷ 115,200 = 434 clock cycles / bit CLKS_HALF_BIT = 434 ÷ 2 = 217 1 bit period = 434 × 20 ns = 8.68 µs 1 byte frame = 10 bits × 8.68 µs = 86.8 µs
In RTL — uart_tx.v / uart_rx.v
localparam CLK_FREQ = 50_000_000; localparam BAUD_RATE = 115_200; localparam CLKS_PER_BIT = CLK_FREQ / BAUD_RATE; // 434 // In DATA state: if (clk_cnt == CLKS_PER_BIT - 1) begin clk_cnt <= 0; shift_reg <= shift_reg >> 1; // LSB first bit_cnt <= bit_cnt + 1; end
8N1 Configuration means:
8
Data Bits
uart_tx.v counts bit_cnt 0→7 (8 states in DATA)
N
No Parity
Parity bit position is skipped entirely — saves 1 bit time
1
Stop Bit
TX returns HIGH for 1 full bit period before next frame
Common Baud Rates (all with 50 MHz clock):
9600
÷5208
19200
÷2604
38400
÷1302
57600
÷868
115200
÷434
230400
÷217
921600
÷54

## Slide 9
Loopback Verification · Verilator Simulation
$ make uart
1. Compile
Verilator builds: uart_tx.v + uart_rx.v uart_top.v + tb_uart_top.v
→
2. Loopback
uart_top.tx wire-connected to uart_top.rx internally (no physical hardware needed)
→
3. Run TB
Testbench sends bytes: "hello deepak" RX captures & compares
→
4. VCD Out
Produces tb_uart.vcd (~2.9 MB waveform file) Open in GTKWave
Expected Terminal Output
[UART TB] Sending byte: 0x68 ('h')
[UART TB] Received: 0x68 ('h') ← PASS
[UART TB] Sending byte: 0x65 ('e')
[UART TB] Received: 0x65 ('e') ← PASS
...
[UART TB] String "hello deepak" verified: ALL PASS
GTKWave Signals to Add
clk — 50 MHz system clock
reset — active-high reset
uart_top.tx — serial output (8N1 frame)
uart_top.tx_state[1:0] — 0=IDLE 1=START 2=DATA 3=STOP
uart_tx.clk_cnt[9:0] — baud counter (0 → 433)
uart_tx.bit_cnt[2:0] — bit counter (0 → 7)
uart_rx.data_valid — 1-cycle pulse per received byte
uart_rx.data_out[7:0] — received byte value
Debug: data_valid never fires → check reset clears rx_sync to 1'b1 | Wrong byte → verify CLKS_PER_BIT matches TX & RX | Framing error → check CLK_FREQ param
Lab Execution — make uart

## Slide 10
Waveform: Decoding a UART Frame in GTKWave
Transmitting 'H' = 0x48 = 0100_1000
Bit
Cycles
Time (ns)
TX Value
Meaning
Bit Value
START
0–433
0–8,680
tx = 0
Start bit (LOW)
—
D0
434–867
8,680–17,360
tx = 0
D0 = 0 (LSB of 0x48)
0
D1
868–1301
17,360–26,040
tx = 0
D1 = 0
0
D2
1302–1735
26,040–34,720
tx = 0
D2 = 0
0
D3
1736–2169
34,720–43,400
tx = 1
D3 = 1
1
D4
2170–2603
43,400–52,060
tx = 0
D4 = 0
0
D5
2604–3037
52,060–60,740
tx = 0
D5 = 0
0
D6
3038–3471
60,740–69,420
tx = 1
D6 = 1
1
D7
3472–3905
69,420–78,100
tx = 0
D7 = 0 (MSB of 0x48)
0
STOP
3906–4339
78,100–86,800
tx = 1
Stop bit (HIGH)
—
Total: 4340 cycles × 20 ns = 86.8 µs | Read D0→D7 LSB-first: 0 0 0 1 0 0 1 0 → reverse = 0100_1000 = 0x48 = 'H' ✓

## Slide 11
Real-World Applications of UART
FT232 / CP2102 USB-UART Bridges
Convert USB to UART for connecting microcontrollers and FPGAs to a host PC serial terminal (PuTTY / screen). The exact interface this project's uart_tx.v would drive.
FPGA Bring-Up & Debug
UART is the first peripheral added to any new SoC or FPGA design — its simplicity makes it the perfect early-stage debug channel. If UART works, the clock tree and basic RTL are correct.
Arduino / STM32 Embedded MCUs
The Serial.print() call on Arduino uses a UART transmitter identical in structure to uart_tx.v — same 8N1 format, same baud rate configuration, same start/stop framing.
THIS Project: PicoRV32 SoC
uart_tx_pin in GTKWave shows the live 8N1 serial stream. tb_top.v UART monitor decodes bytes and prints: [TB] RX byte: H ← verified ✓ 10× 'Hello Deepak from Nielit!' → TEST PASSED

## Slide 12
Key Takeaways
UART Protocol
Asynchronous serial, 2 wires (TX + RX), no clock line — both sides must agree on baud rate
8N1 Format
1 start bit (LOW) + 8 data bits (LSB first) + 1 stop bit (HIGH) — no parity in this project
Baud Calculation
CLKS_PER_BIT = 50,000,000 ÷ 115,200 = 434 clock cycles per bit at 50 MHz system clock
TX FSM
rtl/uart_tx.v — 4 states: IDLE / START / DATA / STOP (bit_cnt 0→7 in DATA state)
RX FSM
rtl/uart_rx.v — mid-bit sampling + 2-FF synchronizer (rx_sync0→rx_sync1) for metastability protection
Lab Command
make uart → loopback → tx_byte == rx_byte → PASS → inspect tb_uart.vcd in GTKWave
Full SoC
UART enabled via AXI write to 0x1000_0000 — uart_axi.v wraps TX+RX with AXI-Lite backpressure