## Slide 1
Sub-module 4
Memory-Mapped I/O
PicoRV32 + UART SoC
How a RISC-V core talks to a UART through memory-mapped I/O
Covers hardware architecture, bus transactions, and firmware
From MMIO concept → bus protocol → register map → C firmware
Notes: 1

## Slide 2
What We'll Cover
01
02
What is MMIO?
PicoRV32 SoC - Complete Memory Map
03
AXI Decode Address
04
Block Diagram: AXI→Decoder→UART
05
Firmware UART Driver — fw/main.c
06
MMIO Write Path: uart_putc(‘H’) Full Trace
07
Lab: make soc_pico_uart_mem
08
Design Rules
09
Summary
Notes: 2

## Slide 3
What is Memory-Mapped I/O?
Analogy:
RISC-V has no special IN/OUT instructions. Every peripheral — including UART — sits at a fixed physical address. The CPU uses ordinary lw / sw instructions; the interconnect routes the access to the right device.
What MMIO Defines
  Fixed physical address per peripheral
  Normal load/store = device access
  No special I/O instructions needed
  Address bus decoded by interconnect
Why It Matters
  Multiple peripherals share one bus
  Avoids data corruption & conflicts
  Enables modular SoC design
  Reusable IP blocks with fixed maps
UART in MMIO World
  UART sits at e.g. 0x10013000
  CPU writes txdata → UART transmits
  CPU reads rxdata → UART receives
  Control regs configure baud, stop bits
Notes: 3

## Slide 4
PicoRV32 SoC - Complete Memory Map
Address Range
Peripheral
Bus
Size
0x0000_0000–
0x0000_FFFF
ROM
AXI-Lite S0
64 KB win / 8 KB deep
0x0001_0000–
0x0001_FFFF
SRAM
AXI-Lite S1
64 KB win / 256 B deep
0x1000_0000
UART TX
AXI-Lite S2
Write → transmit byte
0x1000_0004
UART RX
AXI-Lite S2
Read → received byte
0x1000_0008
UART STATUS
AXI-Lite S2
bit[1] = rx_buf_valid
STATUS Reg — 0x1000_0008
Bit [0]
reserved = 0
Bit [1]
rx_buf_valid — RX byte ready
Bits [31:2]
reserved = 0
axi_decoder.v — casez match
32'h0000_????: sel = 3'b001; // ROM
32'h0001_????: sel = 3'b010; // SRAM
32'h1000_000?: sel = 3'b100; // UART
default: sel = 3'b001; // safe
Notes: 4

## Slide 5
AXI Address Decode — Project Addresses
PicoRV32 AXI Master
▶
AWADDR
/ ARADDR
axi_decoder.v
0x0000_????
3'b001
→ ROM S0
0x0001_????
3'b010
→ SRAM S1
0x1000_000?
3'b100
→ UART S2
default
3'b001
→ ROM safe
wr_sel[2:0] / rd_sel[2:0] — one-hot
▶
sel=3'b001
ROM
S0 — AXI-Lite
0x0000_0000
▶
sel=3'b010
SRAM
S1 — AXI-Lite
0x0001_0000
▶
sel=3'b100
UART
S2 — AXI-Lite
0x1000_0000
Key: Address bits [31:16] select the slave. casez wildcard '?' masks lower nibbles. AXI backpressure: AWREADY/WREADY go LOW when buf_valid=1 (UART busy).
Notes: 5

## Slide 6
SoC Block Diagram — CPU → AXI → Decoder → UART
PicoRV32
CPU
mem_valid
mem_addr
AXI-Lite
Bridge
top.v
AXI
Interconnect
axi_interconnect.v
Address
Decoder
axi_decoder.v
ROM
S0 — 0x0000_????
SRAM
S1 — 0x0001_????
UART
S2 — 0x1000_000?
Signal Flow (AXI Write Path):
① CPU issues mem_valid + mem_addr = 0x1000_0000 on native bus
② AXI bridge translates to m_axi_awaddr + awvalid handshake
③ Interconnect fans out awvalid to all slaves simultaneously
④ Decoder sets wr_sel = 3'b100 → only uart_axi sees awvalid=1
Notes: 6

## Slide 7
MMIO in C — UART Driver (fw/main.c)
fw/main.c
/* UART register macros */
#define UART_TX (*(volatile char*)0x10000000)
#define UART_RX (*(volatile char*)0x10000004)
#define UART_STATUS (*(volatile int*) 0x10000008)
void uart_putc(char c) {
UART_TX = c; /* AXI backpressure stalls CPU */
}
char uart_getc(void) {
while (!(UART_STATUS & 0x2));
return UART_RX; /* clears rx_buf_valid */
}
void uart_puts(const char *s) {
while (*s) uart_putc(*s++);
}
volatile
Prevents compiler from caching the hardware register read/write — MANDATORY for MMIO
uart_putc
Single store instruction to 0x1000_0000. AXI backpressure stalls CPU if buf_valid=1
uart_getc
Polling loop on bit[1]. When STATUS & 0x2 — RX byte is ready. Reading UART_RX clears flag
uart_puts
Iterates through null-terminated string, calling uart_putc for each character
Notes: 8

## Slide 8
MMIO Write Path — uart_putc('H') Step-by-Step
①
C Statement
UART_TX = 'H'; → compiler: lui a0,0x10000 | li a1,0x48 | sb a1,0(a0)
②
PicoRV32 Native Bus
mem_valid=1 mem_addr=0x10000000 mem_wstrb=4'h1 mem_wdata=0x00000048
③
CPU→AXI Bridge (top.v)
m_axi_awaddr=0x10000000 m_axi_wdata=0x48 m_axi_wstrb=4'h1 awvalid=1
④
AXI Interconnect + Decoder
casez: 32'h1000_000? → wr_sel=3'b100 Only uart_axi receives awvalid=1
⑤
uart_axi.v
w_byte ← 0x48 buf_valid ← 1 AWREADY/WREADY go LOW (backpressure active)
⑥
uart_tx.v FSM
IDLE → START → DATA(×8) → STOP Serial bits on tx_out pin at configured baud

## Slide 9
Lab — make soc_pico_uart_mem (MMIO SoC Subsystem)
$ make soc_pico_uart_mem
Architecture (Sub-module 4)
PicoRV32 CPU → direct native bus → UART peripheral
Simpler than full AXI SoC — pure MMIO concept demo
No AXI bridge or interconnect in this variant
Build steps:
① cd fw && make → rom.hex
② Verilator: picorv32_uart_mem/rtl/ + tb/tb_mem_soc.v
③ ROM loaded from +romhex=rtl/rom.hex
④ Simulation → tb_mem_soc.vcd (142 MB)
Tip: vcd2fst for faster GTKWave loading
Expected Output + GTKWave Signals
[TB] RX byte: H
[TB] RX byte: e ... (10 greetings)
[TB] FIFO flushed – sending: PING
[TB] RX byte: P I N G
TEST PASSED
GTKWave key signals:
cpu_mem_addr → 0x1000_0000 (TX writes)
cpu_mem_wstrb → 4'h1 (SB byte store)
cpu_mem_wdata → 0x48 = 'H'
uart_tx → serial bitstream

## Slide 10
Design Rules — MMIO Best Practices
V
volatile is Mandatory
Prevents compiler from caching MMIO register reads/writes. Without it, CPU may never re-read STATUS register inside while loop — the C optimizer will hoist it out of the loop.
1T
One Outstanding Transaction
PicoRV32 is single-issue non-pipelined. Only one mem_valid can be outstanding at any time. No out-of-order or speculative memory access. Keeps AXI handshake straightforward.
AX
AXI Backpressure Rule
AWREADY/WREADY go LOW when uart_axi.buf_valid=1. CPU bridge stalls — no data loss without a FIFO. No explicit wait() needed in firmware; hardware handles flow control.
RT
ASIC-Clean RTL Rule
No initial blocks in RTL. All state must be reset-driven (posedge clk, negedge rst_n). initial blocks are simulation-only; they are ignored by synthesis tools for ASIC.
AL
Address Alignment
AXI-Lite requires word-aligned addresses — bits[1:0] must be 00. Unaligned accesses cause undefined behavior. UART_STATUS at 0x1000_0008 (divisible by 4) is compliant.

## Slide 11
Sub-module 4 - Key Takeaways
MMIO Core Principle:
CPU uses standard load/store to talk to hardware — no special I/O instructions in RISC-V.
Register Map:
0x1000_0000 → UART TX | 0x1000_0004 → UART RX | 0x1000_0008 → STATUS (bit[1]=rx_buf_valid)
volatile is Non-Negotiable:
Prevents compiler from optimizing away hardware register accesses — required for all MMIO pointers.
Firmware Polling:
while (!(UART_STATUS & 0x2)); — polls STATUS register until RX byte is available.
Lab Command:
make soc_pico_uart_mem → direct native bus SoC (no AXI) | make soc → full AXI-Lite SoC.
Notes: 13