## Slide 1
Sub-module 5
RISC-V AXI Integration
PicoRV32 ↔ AXI-Lite Bridge FSM
For learners with RISC-V ISA and AXI4-Lite fundamentals

## Slide 2
What We'll Cover
01
02
Integration Problem Statement
PicoRV32 Native Memory Interface
03
Why Introduce AXI4-Lite?
04
THIS Project’s Bridge — Custom FSM in top.v
05
SoC Architecture Overview
08
AXI Write & Read Transactions
09
Design Rules
10
End-to-End: uart_putc(‘H’) Full Signal Trace
11
Firmware Macros — fw/main.c
06
Bridge FSM: 5 States
07
Bridge Registers & ASIC-Clean Code
12
Lab: make riscv_axi
13
Summary

## Slide 3
Integration Problem Statement
Analogy:
PicoRV32 speaks its own simple handshake language (mem_valid/mem_ready). AXI4-Lite is a richer, industry-standard protocol used by most SoC IP blocks. To connect them, you need a translator — an adapter — just like a plug adapter when travelling abroad.
PicoRV32 Native Bus
• Uses mem_valid to request a transfer
• Waits (stalls) until mem_ready=1
• One transaction at a time — very simple
• No channels, no separate handshakes
The Mismatch
• AXI4-Lite has 5 independent channels
• Each channel has its own VALID/READY
• Most SoC IP only exposes AXI interfaces
• You cannot wire them together directly
The Solution
• Use picorv32_axi wrapper, OR
• Use picorv32 + axi_adapter bridge
• The adapter converts single-channel mem bus → 5-channel AXI
• Rest of SoC sees a clean AXI master
Prerequisites assumed:
✓ RISC-V ISA — you know how lw / sw / store instructions work
✓ AXI4-Lite — you know the 5 channels (AW, W, B, AR, R) and VALID/READY handshake

## Slide 4
PicoRV32 Native Memory Interface
Handshake Rules
1. mem_valid MUST stay HIGH until mem_ready=1 2. mem_wstrb≠0 → Write transaction; =0 → Read transaction 3. One outstanding transaction at a time 4. CATCH_MISALIGN=1 and CATCH_ILLINSN=1 active in this project
Signal | Dir | Width | Description
mem_valid | OUT | 1 | CPU asserts: memory request active
mem_ready | IN | 1 | Slave responds: request accepted
mem_addr | OUT | 32 | Target byte address
mem_wdata | OUT | 32 | Write data (byte-lane aligned)
mem_wstrb | OUT | 4 | Byte enables — non-zero = write, 0 = read
mem_rdata | IN | 32 | Read data from slave
mem_instr | OUT | 1 | Instruction fetch (vs data access)

## Slide 5
Why AXI4-Lite?
①
Industry Standard
AXI4-Lite is ARM AMBA spec — used in Xilinx, Intel, SiFive IP. Familiarity and toolchain support.
②
Simple Subset
No bursts, no out-of-order. Single-beat transfers only — matches PicoRV32's one-outstanding-TX constraint perfectly.
③
Peripheral Ecosystem
AXI-Lite slaves (UART, GPIO, SPI) are readily available and reusable. uart_axi.v drops in without modification.
④
Verifiable Waveforms
5 named channels produce clear GTKWave traces. b_state[2:0] lets students trace every cycle of the handshake.

## Slide 6
This Project's Bridge — Custom FSM in top.v
NOT picorv32_axi wrapper — fully visible custom logic
WHY CUSTOM?
• Native bus stays accessible for debug • Fully visible: rtl/top.v lines 91–224 • Integrates with 3-slave interconnect • ASIC-clean: no initial blocks, no = value initializers • b_state[2:0] observable in GTKWave
BRIDGE SIGNALS (m_axi_*)
// Outputs (CPU → Fabric)
m_axi_awaddr [31:0]
m_axi_awvalid
m_axi_wdata [31:0]
m_axi_wstrb [3:0]
m_axi_wvalid
m_axi_bready
m_axi_araddr [31:0]
m_axi_arvalid
m_axi_rready
// Inputs (Fabric → CPU)
m_axi_awready
m_axi_wready
m_axi_bvalid
m_axi_arready
m_axi_rvalid
m_axi_rdata [31:0]

## Slide 7
SoC Architecture Overview
How the PicoRV32 master, interconnect, and AXI4-Lite slaves fit together
PicoRV32 CPU
↓ mem_valid / mem_ready
CPU-to-AXI Bridge (rtl/top.v lines 91–224)
↓ AXI-Lite 5-channel
AXI-Lite Interconnect (axi_lite_interconnect.v) + Decoder (axi_decoder.v)
S0: ROM
(rom.v)
0x0000_0000
– 0x0000_FFFF
S1: SRAM
(sram.v)
0x0001_0000
– 0x0001_FFFF
S2: UART
(uart_axi.v)
0x1000_0000
– 0x1000_000F

## Slide 8
Bridge FSM: 5 States
b_state[2:0] in rtl/top.v — complete state transitions
3'd0
ST_IDLE
Wait for cpu_mem_valid
wstrb≠0 → ST_WR_AW | wstrb=0 → ST_RD_AR
→
3'd1
ST_WR_AW
Issue awaddr, awvalid, wdata, wvalid=1
Wait awready & wready
If bvalid → ST_IDLE else → ST_WR_B
→
3'd2
ST_WR_B
Wait for bvalid
Assert ready_r=1 → cpu_mem_ready=1
→ ST_IDLE
→
3'd3
ST_RD_AR
Issue araddr, arvalid=1
Wait arready handshake
Assert rready=1 → ST_RD_R
→
3'd4
ST_RD_R
Wait for rvalid
Capture rdata_r ← m_axi_rdata
Assert ready_r=1 → ST_IDLE
Write latency: 3–4 cycles | Read latency: 2–3 cycles | Monitor b_state[2:0] in GTKWave for deadlock detection

## Slide 9
Bridge Registers & ASIC-Clean Code
rtl/top.v — all registers reset-driven, no = initializers
// Bridge state register
reg [2:0] b_state;
// AXI Write outputs
reg [31:0] m_axi_awaddr;
reg m_axi_awvalid;
reg [31:0] m_axi_wdata;
reg [3:0] m_axi_wstrb_r;
reg m_axi_wvalid;
reg m_axi_bready;
// AXI Read outputs
reg [31:0] m_axi_araddr;
reg m_axi_arvalid;
reg m_axi_rready;
// Internal capture
reg [31:0] rdata_r;
reg ready_r; // → cpu_mem_ready
// ASIC-clean reset block
if (reset) begin
b_state <= ST_IDLE;
m_axi_awvalid <= 1'b0;
m_axi_wvalid <= 1'b0;
m_axi_bready <= 1'b0;
m_axi_arvalid <= 1'b0;
m_axi_rready <= 1'b0;
ready_r <= 1'b0;
rdata_r <= 32'h0;
end
// (* keep *) on all bridge wires
// Prevents Yosys pruning during
// synthesis — critical for ASIC flow
// tx_out renamed from uart_tx
// → avoids Yosys scope collision

## Slide 10
AXI Write Transaction
Example: UART TX write → 0x10000000
Cycle 1
AW Channel
AWADDR=0x10000000
AWVALID=1 → AWREADY=1
Address handshake complete
→
Cycle 1
W Channel
WDATA=0x48 ('H')
WSTRB=4'h1 (byte store)
WVALID=1 → WREADY=1
→
Cycle 2
B Channel
BVALID=1
BREADY=1 (asserted by bridge)
BRESP=2'b00 (OKAY)
→
Cycle 3
CPU Done
ready_r=1
cpu_mem_ready=1 (pulse)
b_state → ST_IDLE
Note: WSTRB=4'h1 because firmware uses SB (byte store) for UART. AW and W channels can fire simultaneously.

## Slide 11
AXI Read Transaction
Example: UART TX read→ 0x10000000
Cycle 1
AR Channel
ARADDR=0x10000008
ARVALID=1 → ARREADY=1
Address handshake done
→
Cycle 1
Bridge
b_state: ST_IDLE
→ ST_RD_AR
Assert RREADY=1
→
Cycle 2
R Channel
RVALID=1
RREADY=1
RDATA latched into rdata_r
→
Cycle 3
CPU Done
ready_r=1 pulse
cpu_mem_ready=1
b_state → ST_IDLE
Addresses: UART TX = 0x10000000 | UART RX = 0x10000004 | UART STATUS = 0x10000008

## Slide 12
Design Rules & Gotchas
KEEP
Rule 1 — VALID Stays High
mem_valid MUST remain asserted until mem_ready=1. Dropping valid early causes the slave to abort — CPU hangs waiting.
KEEP
Rule 2 — One Outstanding TX
Bridge supports one in-flight transaction at a time. b_state must return to ST_IDLE before next request is issued.
NEW
Rule 3 — ASIC-Clean Bridge
All bridge registers use reset-driven initialization. No = value initializers in top.v. Verified Yosys-compatible.
NEW
Rule 4 — Trap on Bad Access
CATCH_MISALIGN=1, CATCH_ILLINSN=1 active. CPU traps if bridge fails to respond — prevents silent hang.
NEW
Rule 5 — tx_out Rename
uart_tx renamed to tx_out port in uart_axi.v. Required to avoid Yosys scope collision during synthesis.
NEW
Rule 6 — Deadlock Detection
If b_state stays non-zero > 10 cycles: check slave valid/ready not toggling. Check wr_sel/rd_sel routing in interconnect.

## Slide 13
End-to-End: uart_putc('H') Full Signal Trace
1. Firmware
uart_putc('H')
→ UART_TX = 'H'
→ SB x5,0(x10) [wstrb=4'h1, addr=0x10000000, wdata=0x48]
→
2. Native Bus
CPU asserts:
mem_valid=1, mem_wstrb=4'h1
mem_addr=0x10000000, mem_wdata=0x48
→
3. Bridge FSM
ST_IDLE → ST_WR_AW
awaddr=0x10000000, awvalid=1
wdata=0x48, wstrb=4'h1, wvalid=1
4. Interconnect
wr_sel=3'b100 (UART selected)
uart_axi.s_axi_awvalid=1
Other slaves: awvalid=0
→
5. uart_axi.v
AW handshake → aw_got=1
W handshake → w_byte=0x48, buf_valid=1
BVALID=1, BRESP=2'b00 OKAY
→
6. uart_tx.v
data=0x48, FSM:
START → DATA(×8) → STOP
tx_out: 8N1 @ 115200 baud
Total latency: ~3 cycle bridge transition + 434 cycle UART start bit (115200 baud @ 50 MHz)
From C firmware to serial bit on tx_out

## Slide 14
Firmware Macros — fw/main.c
Project address map and UART API
#define UART_TX (*(volatile char*)0x10000000)
#define UART_RX (*(volatile char*)0x10000004)
#define UART_STATUS (*(volatile int*) 0x10000008)
// No uart_init() needed — uart_axi auto-enabled after reset
static void uart_putc(char c) {
UART_TX = c;
// Generates: SB x5, 0(x10)
// mem_addr=0x10000000, mem_wstrb=4'h1, mem_wdata=c
}
static char uart_getc(void) {
while (!(UART_STATUS & 0x2)); // poll bit[1] RX ready
return UART_RX;
}
Address | Register | Notes
0x10000000 | UART_TX | Byte write → triggers serial TX
0x10000004 | UART_RX | Byte read → receive buffer
0x10000008 | UART_STATUS | bit[0]=TX busy, bit[1]=RX ready
TX FLOW
uart_putc('H')
↓
UART_TX = 0x48
↓
SB x5, 0(x10)
↓
mem_valid=1, wstrb=4'h1
↓
AXI Write → uart_axi.v
↓
tx_out: 8N1 bits

## Slide 15
Lab — RISC-V AXI Integration Demo
make riscv_axi → AXI handshake walk-through
$ make riscv_axi
---- Simulation Start ----
[50 ns] AXI WRITE TRANSACTION
AWADDR=0x10000000, AWVALID=1 → AWREADY=1 → Address accepted
WDATA=0x000000A5, WVALID=1 → WREADY=1 → Data accepted
BVALID=1 → Write OKAY → Transaction complete
Result: 0xA5 written to 0x10000000
[110 ns] AXI READ TRANSACTION
ARADDR=0x10000000, ARVALID=1 → ARREADY=1 → Address accepted
RDATA=0x000000A5, RVALID=1 → RREADY=1 → Data received
Result: Read 0xA5 (matches written value)
Write = Success | Read = Success
---- Simulation End ----
GTKWave Signals
clk, reset
m_awvalid, s_awready
← AW channel
m_wdata, m_wvalid, s_wready
← W channel
s_bvalid, m_bready
← B channel
m_arvalid, s_arready
← AR channel
s_rdata[31:0], s_rvalid
← R channel
b_state[2:0] from tb_top.fst
← Full SoC bridge debug
VCD Output: tb_riscv_axi_lite.vcd (3.3 KB) | Testbench: tb/tb_riscv_axi_lite.v (self-contained)

## Slide 16
Key Takeaways
⚙
Bridge translates mem_valid/mem_ready → 5-channel AXI-Lite. Implemented in rtl/top.v lines 91–224.
↔
Write path: ST_IDLE → ST_WR_AW → ST_WR_B → ST_IDLE | Read path: ST_IDLE → ST_RD_AR → ST_RD_R → ST_IDLE
📁
All bridge registers: m_axi_* — ASIC-clean, reset-driven, no = initializers. b_state[2:0] is the FSM register.
📍
Project addresses: ROM=0x0000_0000 | SRAM=0x0001_0000 | UART TX=0x1000_0000 | RX=0x1000_0004 | STATUS=0x1000_0008
🛠
Lab: make riscv_axi → observe step-by-step AXI handshake log. Testbench: tb/tb_riscv_axi_lite.v
📊
GTKWave: add b_state[2:0], m_axi_awvalid, m_axi_rvalid from tb_top.fst to trace full bridge activity.