## Slide 1
AXI4-LITE UART INTEGRATION
AXI4-Lite UART
Integration
▸ How UART becomes a memory-mapped AXI4-Lite slave
▸ Register layout, write/read transaction flows, and firmware
▸ End-to-end: C code → AXI bus → serial bits on the wire
▸ For learners with UART and AXI4-Lite fundamentals
PREREQUISITES:
✓ UART protocol
✓ AXI4-Lite channels
✓ Basic C / MMIO

## Slide 2
What We'll Cover
01
02
Why UART needs AXI slave interface — MMIO access pattern
uart_axi.v: 3 registers at 0x10000000 / 0x10000004 / 0x10000008
03
Write path: AXI → uart_axi → buf_valid → uart_tx → serial bits
04
Read path: uart_rx → rx_buf_valid → AXI read returns byte
05
Backpressure: AWREADY/WREADY = 0 when buf_valid = 1 (no data loss)
06
Firmware: fw/main.c uart_putc / uart_getc via volatile macros
07
Lab: make axi_uart → AXI master + uart_axi DUT → verify byte transfer

## Slide 3
WHY AXI FOR UART?
3
The Mailbox Analogy
CPU = Person wanting to send a letter
UART registers = Mailbox slots
AXI4-Lite = Standard postal interface
AXI master/slave = Postman + Mailbox
CPU cannot directly drive serial pins — it uses memory-mapped I/O (MMIO). AXI4-Lite provides the standard bus interface for this.
AXI4-Lite Channels
AW
Address Write — CPU sends target address
W
Write Data — CPU sends byte to write
B
Write Response — Slave confirms completion
AR
Address Read — CPU requests register read
R
Read Data — Slave returns value

## Slide 4
Register Map & Internal Architecture — uart_axi.v
Address
Offset
Name
Description
0x1000_0000
0x00
UART TX
Write wdata[7:0] → triggers TX serialisation
0x1000_0004
0x04
UART RX
Read returns {rx_buf_valid, rx_data[7:0]}
0x1000_0008
0x08
STATUS
Read returns {30'b0, rx_buf_valid, 1'b0}
Internal Architecture — uart_axi.v
AXI Write FSM → [1-byte TX buffer] → uart_tx (u_tx) ► tx_out
aw_got / w_got buf_data / buf_valid
uart_rx (u_rx, 2-FF sync) → rx_buf_data / rx_buf_valid → AXI Read FSM
⚠ Backpressure (Critical)
s_axi_awready = !aw_got && !buf_valid
s_axi_wready = !w_got && !buf_valid
→ CPU bridge STALLS when buffer is full → zero data loss

## Slide 5
AXI Backpressure — How uart_axi Prevents Byte Loss
❌ Problem Without Backpressure
CPU sends bytes faster than UART serialises
Bridge time: ~534 cycles
UART byte time: ~4340 cycles (115200 baud)
Without BP: 2nd byte overwrites 1st → data corruption
✅ Solution in uart_axi.v
When buf_valid = 1:
s_axi_awready ← 0 (block new address)
s_axi_wready ← 0 (block new data)
CPU bridge stalls → PicoRV32 waits automatically
AXI Handshake Timeline
buf_valid=1
awready=0
wready=0
→
uart_tx.ready=1
buf_valid←0
→
buf_valid=0
awready=1
wready=1
→
Next byte
Accepted
Handshake OK

## Slide 6
5
AXI Write Transaction — uart_putc('H')
AW
Address Write
AWADDR = 0x10000000
AWVALID = 1
→
W
Write Data
WDATA = 0x48 ('H')
WSTRB = 4'h1 (byte 0)
→
B
Response
BVALID = 1, BRESP = OKAY
cpu_mem_ready ← 1
uart_axi.v Internal Response:
aw_got=1 → w_got=1 → buf_data=0x48, buf_valid=1 → bvalid=1 (OKAY) → uart_tx.valid=1
⚠ Backpressure Note:
AWREADY stays LOW if buf_valid=1 (TX buffer full). CPU bridge waits — no bytes lost. WSTRB=4'h1 (SB instruction → byte 0 only, not 0xF).

## Slide 7
6
AXI Read Transaction — uart_getc()
AR
Address Read
ARADDR = 0x10000008 (STATUS)
or 0x10000004 (RX DATA)
ARVALID = 1
→
R
Read Data
STATUS: RDATA = {30'b0, rx_buf_valid, 1'b0}
RX DATA: RDATA = {23'b0, rx_buf_valid, rx_data[7:0]}
✅ Correct bit interpretation:
bit[1] = rx_buf_valid (NOT bit[31] — that is SiFive FIFO convention, NOT this project)
Firmware polling idiom:
while (!(*(volatile uint32_t*)0x10000008 & 0x2)); // wait for rx_buf_valid
uint8_t c = *(volatile uint32_t*)0x10000004 & 0xFF; // read RX byte

## Slide 8
7
Signal Mapping — CPU → AXI → UART
PicoRV32 CPU
mem_valid=1
mem_addr=0x10000000
mem_wstrb=4'h1
mem_wdata=0x48
→
CPU-to-AXI Bridge
(top.v)
awaddr, awvalid
wdata, wstrb
wvalid
→
AXI Interconnect
(axi_decoder.v)
wr_sel[2:0]=3'b100
→ uart_axi active
→
uart_axi.v
AXI Slave
aw_got, w_got
buf_data, buf_valid
bvalid (OKAY)
→
uart_tx.v
(u_tx)
8N1 serial
115200 baud
tx_out pin
Signal
Direction
Description
mem_wstrb = 4'h1
CPU → Bridge
Byte-write (SB instruction); only byte 0 written
s_axi_awready
uart_axi → Bridge
0 when buf_valid=1 (backpressure)
buf_valid
uart_axi internal
TX buffer occupied; stalls AXI master
tx_out
uart_axi → pin
Renamed from uart_tx to avoid Yosys collision

## Slide 9
SOC ARCHITECTURE
8
PicoRV32
CPU
CPU-to-AXI
Bridge (top.v)
AXI-Lite Interconnect
+ axi_decoder.v
→
→
S0: ROM
(rom.v)
Base: 0x0000_????
Instruction
read-only
S1: SRAM
(sram.v)
Base: 0x0001_????
R/W data
stack, vars
S2: UART
(uart_axi.v)
Base: 0x1000_000?
TX / RX /
STATUS
uart_axi internals: AXI Write FSM → [buf_data/buf_valid] → uart_tx (u_tx) → tx_out | uart_rx (u_rx) → rx_buf_data/rx_buf_valid → AXI Read FSM

## Slide 10
MEMORY MAP - This Project
10
Address
Slave
Register / Purpose
0x0000_????
ROM
Instruction / data — read-only
0x0001_????
SRAM
R/W data — stack, variables
0x1000_0000
UART
TX: write byte to transmit
0x1000_0004
UART
RX: read received byte
0x1000_0008
UART
STATUS: bit[1]=1 means RX byte ready

## Slide 11
DESIGN RULES
11
①
VALID Stays High Until Handshake
Once VALID is asserted, it must not be deasserted until READY is also high. One outstanding TX in-flight.
②
Backpressure — AWREADY/WREADY
uart_axi sets awready/wready=0 when buf_valid=1. CPU bridge waits — no bytes are ever lost, no FIFO needed.
③
Port Rename: tx_out (not uart_tx)
uart_axi instantiates a submodule named uart_tx. A same-name port causes Yosys to lose the wire driver during synthesis. Renamed to tx_out.
④
ASIC-Clean RTL Constraints
No initial blocks, no inline register initializers in uart_axi.v. All state driven by synchronous reset only. Synthesis-safe.
⑤
2-FF Synchroniser in uart_rx
Metastability protection on the incoming serial line. Two flip-flops synchronise the async pin before processing.
⑥
WSTRB = 4'h1 (Byte Write)
SB instruction produces wstrb=4'h1 (byte 0 only), NOT 0xF. uart_axi reads wdata[7:0] only.

## Slide 12
End-to-End Walkthrough — uart_putc('H')
12
1
fw/main.c
uart_putc('H') → UART_TX = 0x48
2
PicoRV32
mem_valid=1, mem_addr=0x10000000, mem_wstrb=4'h1, mem_wdata=0x48
3
CPU-to-AXI Bridge
awaddr=0x10000000, awvalid=1, wdata=0x48, wstrb=4'h1, wvalid=1
4
Interconnect
wr_sel=3'b100 → only uart_axi active
5
uart_axi.v
aw_got=1 → w_got=1 → buf_data=0x48, buf_valid=1
6
uart_axi.v
bvalid=1 (OKAY) → bridge: cpu_mem_ready=1 → CPU resumes
7
uart_tx.v (u_tx)
data=0x48, valid=1 → IDLE→START→DATA(×8)→STOP
8
Serial wire
8N1 frame at 115200 baud → testbench UART monitor decodes 'H'
9
tb_top.v logs: [TB] RX byte: H

## Slide 13
Lab — AXI + UART Integration Testbench
$ make axi_uart
Files Used
rtl/uart_tx.v — TX serialiser
rtl/uart_rx.v — RX + 2-FF sync
rtl/uart_axi.v — AXI slave wrapper
tb/tb_axi_lite_master.v — AXI master tasks
tb/tb_axi_lite.v — master + DUT
What Happens
AXI master writes 0x48 ('H') → 0x10000000
uart_axi buffers → uart_tx serialises → tx_out
uart_rx receives (loopback) → rx_buf_valid=1
Master reads STATUS[1]=1 (RX ready)
Master reads RX=0x48 → WRITE DATA == READ DATA → PASS
Key GTKWave Signals:
s_axi_awaddr / awvalid / awready | s_axi_wdata / wvalid / wready | bvalid | uart_axi.buf_valid | u_tx.state[1:0] | rx_buf_valid | s_axi_rdata

## Slide 14
Key Takeaways
uart_axi.v
AXI-Lite slave wrapper for uart_tx.v + uart_rx.v. 250-line ASIC-clean RTL.
Register Map
TX: 0x1000_0000 | RX: 0x1000_0004 | STATUS: 0x1000_0008
TX Backpressure
awready/wready=0 when buf_valid=1 → zero data loss, no FIFO needed.
RX Status
rx_buf_valid flag in STATUS bit[1]; cleared when RX register is read.
Port Rename
tx_out (not uart_tx) — renamed to avoid Yosys synthesis scope collision.
Lab Command
make axi_uart → byte written → UART serialised → loopback → PASS.