## Slide 1
BEGINNER'S GUIDE TO
Firmware on
PicoRV32 + UART
Bare-metal bring-up, memory maps, UART I/O
and how firmware talks to hardware
From first boot to UART hello world — step by step

## Slide 2
What We'll Cover
01
02
What is Firmware?
THIS Project Firmware File Tree
03
UART MMIO Map
04
Startup Code: crt0.S
05
uart_putc + uart_getc
06
Hello World → uart_puts + echo loop
07
Build System — actual fw/Makefile
08
Lab: make fw → make soc

## Slide 3
What is Firmware?
Analogy
Think of firmware like the instructions printed on a microwave's control panel. The hardware (chip) is the microwave oven. The firmware is the tiny program baked inside that reads button presses and controls the heating element — it runs forever, doesn't need an OS, and talks directly to the chip's pins and registers.
What Firmware Is
A C/assembly program compiled for a specific chip
Runs directly on the CPU — no Linux, no Windows
Stored in on-chip ROM or Flash memory
The very first code the chip executes after reset
What Firmware Does
Sets up the stack, clears memory, copies data
Configures hardware peripherals (UART, GPIO…)
Reads sensors, drives outputs in a tight loop
Handles interrupts when events occur
Why RISC-V / PicoRV32?
PicoRV32 = a tiny RISC-V CPU core for FPGAs
AXI4-Lite bus connects CPU to peripherals
Open-source: you can read every transistor!
Perfect for learning SoC firmware from scratch

## Slide 4
Project Firmware Structure — fw/ Directory
# fw/ directory
fw/
├── main.c
├── crt0.S
├── link.ld
├── Makefile
├── bin2hex.py
├── gen_rom_case.py
├── firmware.elf
├── firmware.bin
└── → ../rtl/rom.hex
Build: make fw
Inspect: riscv32-unknown-elf-objdump -d fw/firmware.elf
Verify: cat rtl/rom.hex
main.c
Greet 10 times then echo loop. Defines UART macros, uart_putc(), uart_getc(), uart_puts(), main().
crt0.S
Startup
Stack init (sp = 0x0001_00FC), BSS zero-fill, call main, trap on return. Runs before main().
link.ld
Linker Script
ROM@0x0, SRAM@0x10000, STACKADDR=0x10100. Controls where each section is placed in memory.
bin2hex.py
Tool
Converts firmware.bin to 4-byte-wide hex format for use with Verilog $readmemh in ROM module.
gen_rom_case.py
Tool
Generates a synthesizable case-ROM Verilog module from rom.hex for ASIC/synthesis flows.
Application

## Slide 5
Firmware MMIO — PicoRV32 SoC Register Map
ROM
0x0000_0000
.text section (firmware instructions)
SRAM
0x0001_0000
stack + global variables
Stack Top
0x0001_00FC
set by STACKADDR in link.ld
UART TX
0x1000_0000
Write → [7:0] = byte to transmit
UART RX
0x1000_0004
Read → [7:0] = byte, [8]=rx_valid
UART STATUS
0x1000_0008
Read → [1]=rx_buf_valid
/* fw/main.c — hardware register definitions */
#define UART_TX (*(volatile char*)0x10000000)
#define UART_RX (*(volatile char*)0x10000004)
#define UART_STATUS (*(volatile int*) 0x10000008)
volatile → tells the compiler:
• DO NOT cache this read in a register • DO NOT reorder or optimize away writes
✅ No uart_init() needed
uart_axi.v auto-enables on reset. Baud rate is compile-time fixed — zero runtime init.
🔄 AXI Backpressure
When TX buf full: AWREADY/WREADY go LOW, CPU bridge stalls — no busy-wait loop needed.

## Slide 6
Startup Code — Before main() • crt0.S
# fw/crt0.S — startup code
.section .text
.global _start
_start:
# 1. Init stack pointer
LUI sp, 0x10 # sp = 0x10000
ADDI sp, sp, 0xFC # sp = 0x100FC
# → STACKADDR = 0x0001_00FC
# 2. Zero BSS segment
LA a0, __bss_start
LA a1, __bss_end
bss_loop:
SW zero, 0(a0)
ADDI a0, a0, 4
BLT a0, a1, bss_loop
# 3. Call main()
CALL main
_exit: J _exit # trap on return
Reset vector
PicoRV32 jumps to 0x0000_0000 (PROGADDR_RESET) — first instruction in ROM
Stack init
LUI + ADDI sets sp = 0x0001_00FC
Defined by STACKADDR in fw/link.ld
BSS zero-fill
Clears BSS segment (globals = 0). In this project BSS = 0 bytes, but the pattern is critical.
Call main()
CALL main — firmware application starts. uart_puts() runs, then echo loop begins.
Trap on return
J _exit — infinite loop. main() should never return; this is a safety net.
PicoRV32: active-LOW reset (resetn) connected in top.v
5
4
3
1
2

## Slide 7
uart_putc + uart_getc — Project API (no FIFO bit)
/* fw/main.c — UART API */
/* ── Register macros ── */
#define UART_TX (*(volatile char*)0x10000000)
#define UART_RX (*(volatile char*)0x10000004)
#define UART_STATUS (*(volatile int*) 0x10000008)
/* ── Transmit one byte ── */
static void uart_putc(char c) {
UART_TX = c;
/* AXI backpressure stalls CPU if buf full */
/* NO busy-wait loop needed! */
}
/* ── Receive one byte ── */
static char uart_getc(void) {
/* Poll STATUS bit[1] = rx_buf_valid */
while (!(UART_STATUS & 0x2));
return UART_RX; /* read clears rx_buf_valid */
}
Why no busy-wait in uart_putc?
When the TX buffer is full, uart_axi.v asserts backpressure: AWREADY and WREADY go LOW. The AXI bridge automatically stalls the CPU write — no software polling required.
Why poll STATUS in uart_getc?
ENABLE_IRQ=0 in this PicoRV32 config — no interrupt support. rx_buf_valid (STATUS bit[1]) must be polled. Reading UART_RX automatically clears the flag.
SiFive vs THIS project
SiFive uses bit[31] (FIFO full flag) + explicit polling. THIS project uses AXI backpressure — uart_putc is one line, not a while-loop wrapper.

## Slide 8
Hello World → uart_puts + Echo Loop
/* fw/main.c — complete application */
static void uart_puts(const char *s) {
while (*s) uart_putc(*s++);
}
int main(void) {
/* Send greeting 10 times */
for (int i = 0; i < 10; i++)
uart_puts("Hello Deepak from Nielit!\n");
/* Echo loop — receive and retransmit */
while (1)
uart_putc(uart_getc());
return 0; /* never reached */
}
Execution Flow
→
Stack + BSS → call main()
→
uart_puts × 10 greeting
→
uart_getc() → uart_putc()
Testbench Verification (tb/tb_top.v)
// Verify 10 greetings:
expect: "Hello Deepak from Nielit!"
// Repeat × 10 ✓
// Send PING, expect echo:
uart.send("PING");
uart.expect("PING"); // ✓
$display("TEST PASSED");
crt0.S
main()
echo loop

## Slide 9
Build System — fw/Makefile
# fw/Makefile — actual project build
CC = riscv32-unknown-elf-gcc
OBJCOPY = riscv32-unknown-elf-objcopy
CFLAGS = -march=rv32i -mabi=ilp32 \
-nostartfiles -nostdlib \
-T link.ld -O2 -Wall
SOURCES = crt0.S main.c
all: firmware.elf firmware.bin rom.hex
firmware.elf: $(SOURCES)
$(CC) $(CFLAGS) -o $@ $(SOURCES)
firmware.bin: firmware.elf
$(OBJCOPY) -O binary $< $@
rom.hex: firmware.bin
python3 bin2hex.py firmware.bin \
> ../rtl/rom.hex
-march=rv32i
Base ISA only — no M/A/F extensions. Matches PicoRV32 config.
-mabi=ilp32
int/long/pointer = 32-bit. No hardware float registers.
-nostartfiles
Don't link GCC's crt0.o — we use our own crt0.S.
-nostdlib
Don't link libc/libm — bare-metal, no stdlib.
-T link.ld
Use our linker script for ROM/SRAM/stack layout.
Firmware Size:
firmware.elf: ~167 bytes total
.text: 132 bytes (~33 instructions)
.data: 35 bytes (hello string)

## Slide 10
MMIO — How Firmware Talks to Hardware
/* soc.h — all hardware addresses in one place */ #define UART0_BASE 0x10013000u /* Byte offsets from UART0_BASE */ #define UART_TXDATA 0x00 /* Write char to send */ #define UART_RXDATA 0x04 /* Read received char */ #define UART_STATUS 0x08 /* TX full / RX empty */ #define UART_BAUDDIV 0x0C /* Clock divider */ #define UART_CTRL 0x10 /* Enable TX / RX */ /* Pointer macro for register access */ #define UART_REG(off) \ (*(volatile uint32_t*)(UART0_BASE+(off)))
TXDATA
0x00
Write = send byte
RXDATA
0x04
Read = received byte
STATUS
0x08
Bit0=TXFULL, Bit1=RXEMPTY
BAUDDIV
0x0C
Baud = clk ÷ BAUDDIV
CTRL
0x10
Bit0=TXEN, Bit1=RXEN
UART_REG(UART_TXDATA) = 'H'; // Sends the letter H over serial!
UART Register Map

## Slide 11
Lab Execution — Building and Running Firmware
1
Build Firmware
make fw
→ riscv32-unknown-elf-gcc (compile + link)
→ objcopy -O binary → firmware.bin
→ python3 bin2hex.py → ../rtl/rom.hex
2
Inspect ELF
riscv32-unknown-elf-objdump -d fw/firmware.elf
→ 00000000 <_start>:
→ lui sp, 0x10 # sp = 0x10000
→ addi sp, sp, -4 # sp = 0x0001_00FC
3
Run SoC Simulation
make soc
→ ROM loads rtl/rom.hex via $readmemh
→ PicoRV32 fetches from 0x0000_0000
→ UART output verified by testbench
4
Confirm TEST PASSED
[Simulation log output]
→ [ROM] loaded from plusarg: rtl/rom.hex
→ [ROM] Loaded 42 words
→ TEST PASSED
Pipeline: make fw → firmware.elf → firmware.bin → rtl/rom.hex → make soc → TEST PASSED