## Slide 1
Sub-module 9
Waveform Analysis
Using Testbenches
From RTL Design to Simulation-Ready Waveforms

## Slide 2
What We'll Cover
01
02
Testbench Fundamentals
Project Testbench Files
03
VCD vs FST Format
04
Lab Commands
06
AXI Handshake in GTKWave
07
UART Frame Decode
08
AXI Handshake in GTKWave
09
Debug Patterns
05
Signal Grouping by Layer

## Slide 3
What is a Testbench?
Analogy: Think of your SoC as a new car engine, and the testbench as the diagnostic rig in the factory. It provides the fuel (clock) and presses the pedals (stimuli) to ensure the engine runs correctly before it ever hits the road.
An extra Verilog module that wraps your DUT (Device Under Test)
Simulation-only — never synthesized to real hardware
Sits outside the design and talks to it via ports
Drives clock, reset, and bus stimuli into the DUT
Observes outputs via waveforms (VCD/FSDB) and logs
Uses assertions ($assert) to auto-check correctness
Why It Matters
Catches bugs before expensive silicon is made
Simulates real-world conditions safely
Required step before tapeout in any SoC project
What It Is
What It Does

## Slide 4
Testbench Skeleton
Step
Task
Generic Verilog
THIS Project (tb_top.v)
01
Define Module
module tb_soc;
module tb_top; // no ports, simulation-only
02
Generate Clock
always #5 clk = ~clk
always #10 clk = ~clk // 50 MHz (10ns half-period)
03
Apply Reset
rstn=0 for N cycles
reset<=1; repeat(10) @(posedge clk); reset<=0;
04
Instantiate DUT
soc_top DUT (…)
top u_dut(.clk(clk),.reset(reset),.uart_tx(uart_tx_pin),.uart_rx(uart_rx_pin));
05
Preload Memory
$readmemh("prog.hex",rom)
ROM gets hex via +romhex=rtl/rom.hex plusarg → DUT's rom.v calls $readmemh
06
UART Monitor
N/A in generic TB
Independent initial begin: uart_monitor — detects falling edge, counts bit periods, builds byte → rx_fifo

## Slide 5
The Simulation Flow
make soc → VCD → FST → GTKWave → Iterate
1
COMPILE
make soc
Verilator --binary --trace
9 RTL files + tb/tb_top.v
→ obj_soc/sim_soc
2
RUN
./obj_soc/sim_soc +romhex=rtl/rom.hex
Executes simulation
Output: tb_top.vcd (147 MB raw VCD)
3
CONVERT
vcd2fst tb_top.vcd tb_top.fst
Compress: 147 MB → ~5 MB (28× smaller)
Faster GTKWave loading
4
INSPECT
make wave OR gtkwave tb_top.fst
GTKWave opens tb_top.fst
5-layer signal analysis
5
ITERATE
Fix RTL → make soc → make wave
Repeat until:
✅ TEST PASSED in console
⚠️ Icarus Verilog, ModelSim, and QuestaSim are NOT used in this course — use Verilator only.
Waveform VCD File Size Reference
make pico
tb_picorv32.vcd
36 KB
make axi_sa
tb_axi_lite_standalone.vcd
3.8 KB
make uart
tb_uart.vcd
2.9 MB
make riscv_axi
tb_riscv_axi_lite.vcd
3.3 KB
make axi_uart
tb_axi_lite.vcd
1.9 MB
make soc
tb_top.vcd → tb_top.fst
147 MB → ~5 MB

## Slide 6
GTKWave Setup: Opening THIS Project's Waveforms
Step-by-step navigation guide
Step 1 — Run Simulation
make soc # compiles + runs + auto-opens GTKWave
# OR manually:
vcd2fst tb_top.vcd tb_top.fst
gtkwave tb_top.fst &
Both commands produce tb_top.fst (compressed for speed)
Step 2 — Load Signal Hierarchy (SST Panel)
Expand: tb_top → u_dut (top module)
├─ (CPU signals: b_state, m_axi_*)
├─ u_cpu (picorv32 core)
├─ u_interconnect (wr_sel, rd_sel)
├─ u_uart (buf_valid, aw_got, w_got)
│ ├─ u_tx (state, clk_cnt, tx)
│ └─ u_rx (state, data_valid)
└─ u_rom, u_sram
Step 3 — GTKWave Navigation Shortcuts
Ctrl+A
Zoom to fit all time
Ctrl+Scroll
Zoom in/out at cursor
T
Place time marker
Ctrl+G
Go to specific time (ns)
Right-click → Highlight
Color-code signal groups
Waveform Files by Lab
make pico → tb_picorv32.vcd (36 KB)
make axi_sa → tb_axi_lite_standalone.vcd (3.8 KB)
make uart → tb_uart.vcd (2.9 MB)
make riscv_axi → tb_riscv_axi_lite.vcd (3.3 KB)
make axi_uart → tb_axi_lite.vcd (1.9 MB)
make soc → tb_top.fst (~5 MB)
💡 Save your layout: File → Write Save File → waveform.gtkw | Reload: gtkwave tb_top.fst -a waveform.gtkw
Once signals are grouped by layer, the layout persists across simulation runs — you only have to arrange them once.

## Slide 7
Layer-by-Layer GTKWave Analysis
Systematic 5-Layer Waveform Inspection Strategy
L1
System Health
clk — clock toggling?
reset — released after ~10 cycles?
uart_tx_pin — transitions visible?
L2
CPU Activity
u_cpu.mem_valid — asserted on every access
u_cpu.mem_instr — HIGH=fetch, LOW=load/store
u_cpu.mem_addr — PC during fetch; data addr during LW/SW
L3
AXI Bridge FSM
b_state[2:0] — 0=IDLE, 1=WR_AW, 3=RD_AR, 4=RD_R
m_axi_awvalid — write address presented
m_axi_bvalid — write response from slave
m_axi_rvalid — read data from slave
L4
Interconnect Routing
wr_sel[2:0] — one-hot: 001=ROM 010=SRAM 100=UART
rd_sel[2:0] — same for reads
wr_active — write transaction in progress
rd_active — read transaction in progress
L5
Peripheral Detail (UART)
uart_axi.buf_valid — TX byte buffered
uart_axi.u_tx.state — 0=IDLE 1=START 2=DATA 3=STOP
uart_axi.u_tx.clk_cnt — baud counter (0→433)
uart_axi.rx_buf_valid — RX byte waiting to be read
Pattern: How to find a UART Byte Transmission
1
Find wr_sel ≠ 0 AND m_axi_awaddr = 0x10000000
This identifies a UART TX write transaction
2
Follow buf_valid = 1 → u_tx.state: 0→1→2→3→…→0
TX state machine cycles through IDLE→START→DATA→STOP
3
Zoom into uart_tx_pin: 10 bit-periods = one complete frame
1 start bit + 8 data bits + 1 stop bit = 4340 cycles = 86.8 µs

## Slide 8
Hands-On: Decode 'H' from uart_tx_pin
1
Find Start Bit
Locate the falling edge of uart_tx_pin (goes 1→0)
Press T to place Marker 1 here
This is the beginning of the UART frame
2
Sample Each Data Bit at Mid-Period
Each bit = 434 cycles = 8.68 µs
Sample at Marker1 + 4.34 µs (half-bit offset) for D0, then +8.68 µs for each subsequent bit
D0: +4.34µs → tx=0 D4: +39.06µs → tx=0
D1: +13.02µs → tx=0 D5: +47.74µs → tx=0
D2: +21.70µs → tx=0 D6: +56.42µs → tx=1
D3: +30.38µs → tx=1 D7: +65.10µs → tx=0
3
Build the Byte
Collect D7:D0 in order (LSB first, but displayed D7→D0):
D7 D6 D5 D4 D3 D2 D1 D0 → 0 1 0 0 1 0 0 0
= 0x48 = 72 decimal = 'H' ✓
4
Verify Stop Bit
After D7, uart_tx_pin returns to 1 for exactly 8.68 µs (stop bit), then stays HIGH (idle line). If the line doesn't return high, a framing error has occurred.
💡 This is exactly what the UART monitor in tb_top.v does automatically — the uart_monitor initial block decodes each byte the same way!

## Slide 9
Timing Reference Table
50 MHz clock (20 ns/cycle) · 115200 baud · 434 cycles/bit · 4340 cycles/frame
Event
Time
Cycles
Reset released
~0 ns
0
First instruction fetch
~200 ns
10
First UART TX 'H' starts
~3–5 µs
150–250
UART start bit duration
8.68 µs
434
UART full frame (8N1, 10 bits)
86.8 µs
4,340
UART byte with overhead
~90 µs
~4,500
"Hello Deepak from Nielit!" (26 chars)
~2.3 ms
~115,000
10 greeting messages
~23 ms
~1,150,000
PING phase start
~23 ms
~1,150,000
4 PING bytes (P,I,N,G)
~0.4 ms
~20,000
TEST PASSED logged
~23.4 ms
~1,170,000
$finish (Verilator)
~23.4 ms
—
Wall time (Verilator execution)
~1.2 s
—
Formula: cycles_per_bit = CLK_FREQ / BAUD_RATE = 50,000,000 / 115,200 = 434 | frame_cycles = 434 × 10 bits = 4,340 | frame_time = 4,340 × 20ns = 86.8 µs

## Slide 10
Reading AXI Waveforms
🏆 Golden Rule: A transfer occurs ONLY when both VALID=1 AND READY=1 on the same rising clock edge — neither alone is sufficient.
AW
Write Address
Master:
m_axi_awvalid / m_axi_awready
Slave:
s2_axi_awvalid / s2_axi_awready
CPU → Interconnect → UART Slave
Presents write address 0x10000000
W
Write Data
Master:
m_axi_wvalid / m_axi_wready
Slave:
s2_axi_wvalid / s2_axi_wready
Carries actual byte value
wstrb=4'h1 for byte lane 0
B
Write Response
Master:
m_axi_bready
Slave:
s2_axi_bvalid
Slave acknowledges write done
b_state returns to IDLE
AR
Read Address
Master:
m_axi_arvalid / m_axi_arready
Slave:
s2_axi_arvalid / s2_axi_arready
Read from STATUS: 0x10000008
Read from RX data: 0x10000004
R
Read Data
Master:
m_axi_rvalid / m_axi_rready
Slave:
s2_axi_rvalid / s2_axi_rready
Returns register value to CPU
b_state → RD_R → IDLE
Routing Signals & Address Map
Signal
Value
Meaning
wr_sel[2:0]
3'b001
ROM selected for write
wr_sel[2:0]
3'b010
SRAM selected for write
wr_sel[2:0]
3'b100
UART selected for write
m_axi_awaddr
0x10000000
UART TX register (write target)
m_axi_araddr
0x10000008
UART STATUS register (poll RX ready)
m_axi_araddr
0x10000004
UART RX data register

## Slide 11
CPU Fetch vs. UART Transmission
Project Signal Names + Timing Reference
CPU Instruction Fetch
cpu_mem_valid = 1
cpu_mem_instr = 1 // fetch active
cpu_mem_addr[31:0] // incrementing by 4
e.g. 0x0 → 0x4 → 0x8 → 0xC ...
b_state[2:0]: 0 → 3 → 4 → 0
IDLE → RD_AR → RD_R → IDLE
rd_sel[2:0] = 3'b001 // ROM selected
cpu_mem_rdata: RISC-V opcode
e.g. 0x00020137 = LUI x2, 0x20
Key Pattern:
Every ROM read: b_state cycles 0→3→4→0 in 2 clock cycles. rd_sel = 3'b001 confirms ROM is the target. Watch cpu_mem_addr increment by 4 (word-aligned RISC-V instructions).
Reset → First fetch: ~200 ns (10 cycles)
Boot complete: ~3–5 µs (150–250 cycles)
UART Byte Transmission
cpu_mem_addr = 0x10000000
wstrb = 4'h1 // byte lane 0
b_state: 0 → 1 → 0 // IDLE→WR_AW→IDLE
wr_sel = 3'b100 // UART selected
uart_axi.buf_valid = 1 // TX buffer loaded
uart_axi.u_tx.state:
0→1→2→3→0 (IDLE→START→DATA→STOP→IDLE)
uart_tx_pin:
falling edge (start) → 8 bits → high (stop)
Key Pattern:
UART TX write: b_state cycles 0→1→0 (simpler than read — no read-data phase). wr_sel = 3'b100 confirms UART. buf_valid pulses high when TX byte is latched.
1 bit = 434 cycles = 8.68 µs
1 frame = 4340 cycles = 86.8 µs (8N1)
10 msgs = ~23 ms = ~1,150,000 cycles

## Slide 12
Interactive Debugging
Three Real Bugs from THIS Project — Find & Fix
BUG 1
Simulation passes but no '[TB] RX byte:' output
ROOT CAUSE
byte_logger block not synced — delta-cycle race on rx_fifo
FIX / DEBUG STEPS
independent byte_logger initial block in tb_top.v
while (log_ptr == rx_wr_ptr) #10; // wait for new fifo
$display("[TB] RX byte: %c", rx_fifo[log_ptr & 63]);
LESSON LEARNED
Concurrent Verilog blocks can have delta-cycle races; #10 delay separates logger from monitor safely.
BUG 2
Bridge stuck in state ST_WR_AW (b_state = 1 forever)
ROOT CAUSE
Interconnect wr_sel = 3'b000 — address not decoded
FIX / DEBUG STEPS
In GTKWave: check wr_sel[2:0] when awaddr is presented
Verify axi_decoder.v casez pattern matches the address
Expected: wr_sel = 3'b100 for addr 0x10000000
LESSON LEARNED
A hung b_state means the slave's awready never arrived — always check wr_sel routing first.
BUG 3
TEST FAILED — echo byte wrong or zero
ROOT CAUSE
uart_rx_pin driven wrong — testbench timing off
FIX / DEBUG STEPS
Check uart_axi.u_rx.data_valid pulse width in waveform
Check uart_axi.rx_buf_data value at data_valid=1
Verify TB sends PING with correct BAUD_FULL interval
LESSON LEARNED
TX→RX loopback timing must account for uart_rx latency (4340 cycles = 86.8 µs per byte).
Interview Q: "You see b_state stuck at 1 — what do you check?" → Answer: Check wr_sel routing → slave awready response → slave FSM → backpressure condition
Interview Q: "How do you verify an AXI write completed?" → Answer: AWVALID+AWREADY=1 (AW done), WVALID+WREADY=1 (W done), BVALID+BREADY=1 (B done)

## Slide 13
Sub-module 9 — Complete Lab Reference
All waveform files from all modules + Interview Q&A
Sub-module
Command
VCD / FST File
Key Signals
M1
make pico
tb_picorv32.vcd (36 KB)
mem_valid, mem_instr, mem_addr
M2
make axi_sa
tb_axi_lite_standalone.vcd (3.8 KB)
awvalid, awready, rdata
M3
make uart
tb_uart.vcd (2.9 MB)
tx, rx, state, clk_cnt
M4
make soc_pico_uart_mem
tb_mem_soc.fst (142 MB raw)
cpu_mem_addr, mem_wstrb
M5
make riscv_axi
tb_riscv_axi_lite.vcd (3.3 KB)
b_state, m_awvalid, s_rdata
M6
make axi_uart
tb_axi_lite.vcd (1.9 MB)
buf_valid, aw_got, u_tx.state
M7
make fw + wave
tb_top.fst
rom fetch trace in waveform
M8
make soc
tb_top.fst (~5 MB)
full 5-layer analysis
M9 ★
make wave
tb_top.fst (~5 MB)
all layers + UART decode exercise
Interview Questions — Waveform Analysis
Q1: How do you verify an AXI write completed?
A: AWVALID+AWREADY=1 → WVALID+WREADY=1 → BVALID+BREADY=1
Q2: How do you confirm a UART byte was transmitted correctly?
A: Count falling edge, sample 8 bits at CLKS_HALF + n×CLKS_PER_BIT, compare to expected value
Q3: You see b_state stuck at 1 — what do you check?
A: wr_sel routing → slave awready → slave FSM state → backpressure condition